## Slide 2
Andrew Shapton 2021
July 2021
https://github.com/alshapton/Pyntel4004
Assembly Language
Programming Manual

## Slide 4
0 0 0 1 C1 C2 C3 C4
A2 A2 A2 A2 A1 A1 A1 A1
If C1C2C3C4 is true:
A2A2A2A2 PM A1A1A1A1 PL
PH unchanged if C1C2C3C4 is false: (PH) PH
(PM) PM
(PL + 2) PL
C1 C2 C3 C4
Jump if the 4004 Test Signal is = 0
Jump if the Carry Bit is = 1
If the indicated Condition Bit is = 1:
Jump if the Accumulator = 0
Invert ALL the other conditions
JCN
JUMP = C1 * ((ACC = 0) * C2 + (carry = 1) * C3 + TEST * C4 +
C1 * (((ACC <> 0) + C2 ) + ((carry = 0) + C3 ) * (TEST + C4 )

## Slide 5
000 for register pair 0 or 0P
001 for register pair 2 or 1P
010 for register pair 4 or 2P
011 for register pair 6 or 3P
100 for register pair 8 or 4P
101 for register pair 10 or 5P
110 for register pair 12 or 6P
111 for register pair 14 or 7P
0 0 1 0 Rp Rp Rp 0
D1 D2D3 D4 D5 D6 D7D8
8-bit data quantity
SRC 1
D1D2D3D4
D5D6D7D8
Rp Rp Rp Rp
Rp+1 Rp+1 Rp+1 Rp+1
000 for register pair 0 or 0P
001 for register pair 2 or 1P
010 for register pair 4 or 2P
011 for register pair 6 or 3P
100 for register pair 8 or 4P
101 for register pair 10 or 5P
110 for register pair 12 or 6P
111 for register pair 14 or 7P
0 0 1 0 Rp Rp Rp 0
(RRRO) --> DB (X2) (RRR1) --> DB (X3)
(RPp)
DB(x2)
DB(x3)
(RPp+1)
FIM

## Slide 6
SRC 2
1 of 4 DATA RAM chips within the DATA RAM bank previously selected with a DCL instruction
When referring to a DATA Ram character
1 of 4 registers within the DATA RAM chip
1 of 16 characters within the register
1 of 4 DATA RAM chips within the DATA RAM bank previously selected with a DCL instruction
When referring to a DATA RAM status character
1 of 4 registers within the DATA RAM chip
Not relevant

## Slide 7
SRC 3
The port associated with 1 of 4 DATA RAM chips within the DATA RAM bank previously selected by a DCL instruction.
When referring to RAM output port
Not relevant
When referring to a ROM input/output port
Not relevant
The port associated with 1 of 16 ROMs.

## Slide 8
JIN
000 for register pair 0 or 0P
001 for register pair 2 or 1P
010 for register pair 4 or 2P
011 for register pair 6 or 3P
100 for register pair 8 or 4P
101 for register pair 10 or 5P
110 for register pair 12 or 6P
111 for register pair 14 or 7P
0 0 1 1 Rp Rp Rp 1
PM
Rp Rp Rp Rp
Rp+1 Rp+1 Rp+1 Rp+1
PL
PH
PH
unchanged
0 1 0 0 A3 A3 A3 A3
A2 A2 A2 A2 A1 A1 A1 A1
12-bit address
JUN
PM
PL
PH
A3 A3 A3 A3
A2 A2 A2 A2
A1 A1 A1 A1

## Slide 9
FIN
000 for register pair 0 or 0P
001 for register pair 2 or 1P
010 for register pair 4 or 2P
011 for register pair 6 or 3P
100 for register pair 8 or 4P
101 for register pair 10 or 5P
110 for register pair 12 or 6P
111 for register pair 14 or 7P
0 0 1 1 Rp Rp Rp 0
( (PH) . (R0) . (R1) ) RPp
( (PH+1) . (R0) . (R1) ) RPp
OR
JMS
0 1 0 1 A3 A3 A3 A3
A2 A2 A2 A2 A1 A1 A1 A1
12-bit address
PM
PL
PH
A3 A3 A3 A3
A2 A2 A2 A2
A1 A1 A1 A1

## Slide 10
INC
0000 for Register 0
0001 for Register 1
0010 for Register 2
0011 for Register 3
0100 for Register 4
0101 for Register 5
0110 for Register 6
0111 for Register 7
1000 for Register 8
1001 for Register 9
1010 for Register 10
1011 for Register 11
1100 for Register 12
1101 for Register 13
1110 for Register 14
1111 for Register 15
0 1 1 0 R R R R
ISZ
PM
PL
PH
A3 A3 A3 A3
A2 A2 A2 A2
A1 A1 A1 A1
( (PH) . (R0) . (R1) ) RPp
( (PH+1) . (R0) . (R1) ) RPp
OR
RRRR
(RRRR) + 1
A2 A2 A2 A2 A1 A1 A1 A1
8-bit address
0000 for Register 0
0001 for Register 1
0010 for Register 2
0011 for Register 3
0100 for Register 4
0101 for Register 5
0110 for Register 6
0111 for Register 7
1000 for Register 8
1001 for Register 9
1010 for Register 10
1011 for Register 11
1100 for Register 12
1101 for Register 13
1110 for Register 14
1111 for Register 15
0 1 1 1 R R R R
RRRR
(RRRR) + 1
If result = 0
PH
(PH)
PM
(PM)
PL
(PL+2)
If result <> 0
PH
(PH)
(A2 A2 A2 A2)
PL
PM
(A1 A1 A1 A1)

## Slide 11
ADD
0000 for Register 0
0001 for Register 1
0010 for Register 2
0011 for Register 3
0100 for Register 4
0101 for Register 5
0110 for Register 6
0111 for Register 7
1000 for Register 8
1001 for Register 9
1010 for Register 10
1011 for Register 11
1100 for Register 12
1101 for Register 13
1110 for Register 14
1111 for Register 15
1 0 0 0 R R R R
SUB
(RRRR) + (ACC) + (CY) ACC, CY
(ACC) + (RRRR) + (CY) ACC, CY
0000 for Register 0
0001 for Register 1
0010 for Register 2
0011 for Register 3
0100 for Register 4
0101 for Register 5
0110 for Register 6
0111 for Register 7
1000 for Register 8
1001 for Register 9
1010 for Register 10
1011 for Register 11
1100 for Register 12
1101 for Register 13
1110 for Register 14
1111 for Register 15
1 0 0 1 R R R R

## Slide 12
WRn
000 for Character 0
001 for Character 1
010 for Character 2
011 for Character 3
1 1 1 0 1 S S S
0000 for Register 0
0001 for Register 1
0010 for Register 2
0011 for Register 3
0100 for Register 4
0101 for Register 5
0110 for Register 6
0111 for Register 7
1000 for Register 8
1001 for Register 9
1010 for Register 10
1011 for Register 11
1100 for Register 12
1101 for Register 13
1110 for Register 14
1111 for Register 15
LD
1 0 1 0 R R R R
WRM
1 1 1 0 0 0 0 0
M
(ACC)

## Slide 13
BBL
4-bit data item
1 1 0 0 D D D D
XCH
0000 for Register 0
0001 for Register 1
0010 for Register 2
0011 for Register 3
0100 for Register 4
0101 for Register 5
0110 for Register 6
0111 for Register 7
1000 for Register 8
1001 for Register 9
1010 for Register 10
1011 for Register 11
1100 for Register 12
1101 for Register 13
1110 for Register 14
1111 for Register 15
1 0 1 1 R R R R
ACC
(RRRR)
ACBR
(ACC)
RRRR
(ACBR)
ACC
DDDD
PL, PM, PH
(Stack)
LDM
4-bit data item
1 1 0 1 D D D D
ACC
DDDD

## Slide 14
WRR
WPM
(PRAM)
(ACC)
1 1 1 0 0 0 1 1
Data RAM Chip 0 Program RAM
Register 0
Register 1
Register 2
Register 3
Status Characters
4 A B
0x4AA
0x4AB
0x4AC
0x4AD
0x4AE
0x4A9
1 1 1 0 0 0 0 1
RAM Output Register
(ACC)
WMP
1 1 1 0 0 0 1 0
ROM Output Lines
(ACC)
CLB
1 1 1 1 0 0 0 0
ACC
0
CY
0

## Slide 15
A2 A2 A2 A2 A1 A1 A1 A1
12-bit address
PM
PL
PH
A3 A3 A3 A3
A2 A2 A2 A2
A1 A1 A1 A1
( (PH) . (R0) . (R1) ) RPp
( (PH+1) . (R0) . (R1) ) RPp
OR
(ACC) + (RRRR) + (CY) ACC, CY
(ACC) --> MS0
(ACC) MSn
(RRRR) --> ACC
STC
1 1 1 1 0 0 0 1
CLC
1 1 1 1 1 0 1 0
TCC
1 1 1 1 0 1 1 1
CY
0
CY
1
ACC
0
a0
(CY)
CY
0
Least significant bit of the accumulator

## Slide 16
000 for Character 0
001 for Character 1
010 for Character 2
011 for Character 3
1 1 1 0 1 S S S
A2 A2 A2 A2 A1 A1 A1 A1
12-bit address
PM
PL
PH
A3 A3 A3 A3
A2 A2 A2 A2
A1 A1 A1 A1
( (PH) . (R0) . (R1) ) RPp
( (PH+1) . (R0) . (R1) ) RPp
OR
(ACC) + (RRRR) + (CY) ACC, CY
(ACC) --> MS0
(ACC) MSn
(RRRR) --> ACC

## Slide 17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
i4004
Reset
Test
CM-ROM
VDD
CM-RAM3
CM-RAM2
CM-RAM1
CM-RAM0
Memory
Control
Output
Memory
Control
Outputs
VSS
Clk Phase 1
Clk Phase 2
Sync-Out
D3
D2
D1
D0
Data
Bus
I/O
1
2
16
15
3
4
14
13
5
6
12
11
7
8
10
9
PINS
Introduction date: |  | November 15, 1971
Type: |  | 4-bit microprocessor (8-bit instructions)
Frequency: |  | 500KHz - 740KHz
Technology: |  | P-channel silicon gate MOS technology
Number of transistors: |  | 2,300 (10 microns)
Addressable Memory |  | 4096x8-bit ROM and 1280x4-bit RAM
Number of Instructions |  | 45 with a 4 level stack and sixteen 4-bit (or eight 8-bit) registers
History: |  | In 1969 Busicom asked Intel to design a set of chips to be used in a new high perfomance calculator. Ted Hoff, Federico Faggin and Stan Mazor came up with a design that involved a central processing unit, 4004 (CPU) a read-only memory, 4001 (ROM) a random access memory, 4002 (RAM) and a shift register, 4003 (I/O). The CPU was eventually to be called a microprocessor. Later Intel negotiated for a return of the rights for the chips, which had gone to Busicom in the original contract.
Second source: |  | National Semiconductors was the only second source to Intel 4004.

## Slide 18
TIMING
INDEX REGISTER
16 X 4 RAM
DATA
BUS
I/O
BUFFER
SYNC
⏀1
⏀2
D0
D1
D2
D3
RESET
1
2
3
4
8
16
15
14
13
6
7
9
11
Intel 4004
4-BIIT
ADDER
AND SHIFTER
VDD
GND
12
5
PROGRAM COUNTER & STACK
4 X 12 RAM
INSTRUCTION
DECODER
INSTRUCTION
REGISTER
OPR
OPA
INSTRUCTION
DECODER
CY
ACC
CONTROL
CM LOGIC AND BUFFERS
CONTROL
CM REGISTER
INCREMENTER
10
TEST
CM-ROM
CM-RAM0
CM-RAM0
CM-RAM0
CM-RAM0

## Slide 19
Introduction date: |  | 1971
Type: |  | 10-bit Serial-in/Parallel-out, Serial-out Shift Register.
Memory: |  | 256 x 8-bit
Technology: |  | P-channel silicon gate MOS technology
Number of transistors: |  | 
History: |  | The 4003 was designed to be used with other MCS-4/40 devices such as the 4004 CPU.
Second Source |  | National Semiconductors was the only second source.
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
i4003
Q9
O2
O1
O0
VSS
Clock Pulse Input
Serial Out
Q1
Q0
Data In
Parallel
Output
Parallel
Output
Enable Input
Q2
Q3
Q4
Q5
Q6
Q7
Q8
Parallel
Output
1
2
16
15
3
4
14
13
5
6
12
11
7
8
10
9
PINS

## Slide 20
POWER ON CLEAR
BINARY GEN. & DELAY
ENABLE GATES
DATA IN
3
4
2
11
13
6
7
Intel 4003
DELAY
10 BIT SHIFT REGISTER
15
SERIAL OUT
CP
CP
E
16
CP
1
8
9
10
12
Q0
Q1
Q2
Q3
Q4
Q5
Q6
Q7
Q8
Q9
VDD
GND
14
5

## Slide 21
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
i4002
Reset
P0
CM
VDD
O3
O2
O1
O0
Memory
Control
Input
Output
Lines
VSS
Clk Phase 1
Clk Phase 2
Sync-Out
D3
D2
D1
D0
Data
Bus
I/O
Chip Select
Input
Introduction date: | 1971
Type: | 320-bit MOS RAM and 4-bit output port.
Memory: | 80 x 4-bit
Technology: | P-channel silicon gate MOS technology
History: | The 4002 was designed to be used with other MCS-4/40 devices such as the 4004 CPU. The chip was available in two different metal options 4002-1 and 4002-2 this was to make it possible to extend the chip selection so that 4pcs of 4002 chips could be connected to the 4004 CPU without any external chip selection logic.
Second source: | National Semiconductors was the only second source.
1
2
16
15
3
4
14
13
5
6
12
11
7
8
10
9
PINS

## Slide 22
TIMING
RAM
ARRAY
4 X 20 X 4
DATA
BUS
I/O
BUFFER
MUX
INSTRUCTION DECODE & CONTROL
OUTPUT PORT
SYNC
⏀1
⏀2
D0
D1
D2
D3
I/O0
I/O1
I/O2
I/O3
RESET
CM
1
2
3
4
8
16
15
14
13
6
7
9
11
Intel 4002
REFRESH
COUNTER
ADDRESS
MUX
ADDRESS
REGISTER
DECODER
P0
10
R/W
VDD
GND
12
5
Register 0
4-bits
STATUS CHARACTERS
0 THROUGH 3
MAIN MEMORY CHARACTERS
0 THROUGH 15
MEMORY CHARACTER 0
MEMORY CHARACTER 15
STATUS CHARACTER 0
STATUS CHARACTER 3
ONE OF THE 4 REGISTERS
IN THE RAM ARRAY
D3 D2
Chip #
(0 through 3)
D1 D0
Register #
(0 through 3)
D3 D2 D1 D0
Main Memory Character #
(0 through 15)
X2
X3

## Slide 24
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
i4001
Reset
P0
CM
-15v VDD
O3
O2
O1
O0
Memory
Control
Input
Output
Lines
VSS
Clk Phase 1
Clk Phase 2
Sync-Out
D3
D2
D1
D0
Data
Bus
I/O
Clear input
I/O Lines
Introduction date: | 1971
Type: | Fully Decoded Static Random Access Memory..
Memory: | 256 x 8-bit
Technology: | P-channel silicon gate MOS technology (10 microns)
Number of transistors: | 
History: | The 4001 is a 256 x 8-bit ROM designed to be used with other MCS-4/40 devices such as the 4004 CPU.
1
2
16
15
3
4
14
13
5
6
12
11
7
8
10
9
PINS

## Slide 25
TIMING
ADDRESS
REGISTER
AND
DECODER
ROM
ARRAY
16 X 16 X 8
DATA
BUS
I/O
BUFFER
MUX
CONTROL
INPUT PORT
OUTPUT PORT
SYNC
⏀1
⏀2
D0
D1
D2
D3
CM
I/O0
I/O1
I/O2
I/O3
CL
RESET
VDD
GND
1
2
3
4
8
11
16
15
14
13
6
7
10
9
12
5
Intel 4001

## Slide 26
0 240 clb
1 17, 1 jcn(1,1)
3 80, 176 jms(176)
5 81, 95 jms(95)
7 173 ld(13)
8 177 xch(1)
9 240 clb
10 81, 95 jms(95)
12 173 ld(13)
13 28, 41 jcn(12,41)
15 104 inc(8)
16 81, 115 jms(115)
18 39 src(3)
19 236 rd0
20 245 ral
21 179 xch(3)
22 104 inc(8)
23 240 clb
24 81, 160 jms(160)
26 243 cmc
27 179 xch(3)
28 245 ral
29 225 wmp
30 102 inc(6)
31 39 src(3)
32 234 rdr
000 clb
001 jcn TZ $001
003 jms $0b0
005 jms $15f
007 ld 13
008 xch 1
009 clb
00a jms $15f
00c ld 13
00d jcn AN $029
00f inc 8
010 jms $173
012 src 3<
013 rd0
014 ral
015 xch 3
016 inc 8
017 clb
018 jms $1a0
01a cmc
01b xch 3
01c ral
01d wmp
01e inc 6
01f src 3<
020 rdr
Output from Busicom-141PF Calculator ROM disassembly - First 32 words
* https://www.4004.com/2009/Busicom-141PF-Calculator_asm_rel-1-0-1.txt
Pyntel4004 Disassembler
Source Code *